## Slide 1
ML-Driven EEG Biomarkers in DBS Patients
A Hybrid Artifact Removal and Beta-Band Biomarker Extraction Pipeline
Wanghley Soares Martins de Lima | Advisor: Eda Okay, Ph.D. | Duke University Independent Study | Spring 2026
DUKE
Pratt School of Engineering
ECE / BME Independent Study | 2026
INTRODUCTION
Deep Brain Stimulation (DBS) & the EEG Challenge
Deep Brain Stimulation delivers continuous 7 Hz (and harmonics: 14, 21, 28 Hz) electrical pulses via implanted electrodes targeting the subthalamic nucleus (STN) for Parkinson's disease.
These pulses create broadband artifacts that saturate scalp EEG, masking the very biomarkers — beta-band power (13–30 Hz) and phase-amplitude coupling — needed to assess therapeutic state.
Dataset: Patient XU recordings at 3 DBS frequencies (7 Hz, 60 Hz, 100 Hz), sampled at 256 Hz, 19-channel 10-20 montage, matched awake/sleep conditions.
Motivation & Objectives
Develop a clinically viable artifact removal pipeline that preserves endogenous beta oscillations critical for DBS closed-loop control.
Validate a hybrid SVD + NLMS + Spectral Hampel removal sequence on paired DBS-on vs. DBS-off EEG epochs.
Extract and classify biomarkers (beta power, PAC) using supervised ML to distinguish clinical states (awake vs. sleep).
Benchmark all methods quantitatively: harmonic attenuation (dB), broadband spectral preservation (%), and beta-band retention.
STANDARD PREPROCESSING
Four-Stage Consensus Pipeline (MNE 1.10.2 / SciPy)
Stage 1: Zero-Phase FIR Bandpass
Highpass: 0.5 Hz, transition bandwidth 0.25 Hz (MNE l_trans_bandwidth=0.25)
Lowpass: 45 Hz, removes slow drift and high-frequency noise
Zero-phase filtfilt prevents group-delay distortion of event-related potentials
Stage 2: Common Average Reference (CAR)
Subtracts mean potential across all 19 electrodes per time sample
Reduces common-mode noise; improves spatial specificity of subsequent filtering
Stage 3: Notch Filter (60 Hz + Harmonics)
IIR notch at 60 Hz, 120 Hz, 180 Hz (power line); notch width = 1.0 Hz
Q-factor selected to maximize line noise rejection while preserving gamma-band EEG
Stage 4: Anti-Aliasing via Resampling
Decimate to analysis rate (256 Hz) with polyphase anti-aliasing FIR
Applied after ICA to prevent fold-over of DBS harmonics into low bands
ICA: Mutual Information Artifact Rejection
FastICA, n_components=0.95 variance explained; random_state=42
IC rejection: ICLabel probability threshold + EOG correlation (r > 0.7) + muscle power heuristic (>40% power in 20–40 Hz)
RAW EDF
→
BANDPASS 0.5–45 Hz
→
CAR
→
NOTCH 60 Hz
→
RESAMPLE 256 Hz
→
ICA Reject
[ FIGURE: Band Preservation Heatmap ]
Heatmap: methods × frequency bands Rows: Zapline / Spectrum-Fit / Freq-Hampel / Time-Hampel Cols: δ / θ / α / β / γ bands Color scale: 0–100% preservation Source: results/metrics/band_preservation_awake.csv
[ FIGURE: 19-Ch Topographic Maps ]
MNE scalp topomaps: beta-band power Top row: DBS-on (7 Hz, patient XU) Bottom row: DBS-off (baseline) Standard 10-20 montage, mV²/Hz scale Source: results/figures/topomaps_beta.png
SPECIALIZED DBS ARTIFACT REMOVAL
Hybrid Three-Stage DBS Removal Pipeline
Sequential application: SVD Subspace Projection → NLMS Adaptive Filter → Complex Spectral Hampel Interpolation
Stage A: SVD Subspace Projection
Models the DBS artifact as a low-rank sinusoidal subspace using Singular Value Decomposition across channels × time windows.
Design matrix spans exact-frequency sinusoids at all harmonics k·f₀ (k=1…K up to Nyquist): x_dbs(t) = Σ [Aₖ sin(2πkf₀t) + Bₖ cos(2πkf₀t)]
Ordinary Least Squares (QR factorization) per channel fits coefficients; reconstructed DBS model is subtracted. Brain signals not phase-locked to DBS are mathematically orthogonal → preserved.
Chunk mode (chunk_sec configurable): applied in non-overlapping windows for non-stationary DBS frequency drift > 0.01 Hz.
Stage B: NLMS Adaptive Filtering
Normalized Least Mean Squares adaptive filter: w(n+1) = w(n) + μ·e(n)·x(n) / [‖x(n)‖² + ε], targeting residual DBS harmonics after SVD.
Spatiotemporal filter — uses eigendecomposition (np.linalg.eigh) of the STFT covariance matrix per harmonic band to identify the artifact subspace across channels.
Top 1–2 eigenvectors (n_artifact_vecs = max(1, n_ch//2)) define the artifact subspace; projection coefficient = 0.8 removes ~80% of artifact power while retaining correlated brain signals.
Parameters: f_target (auto-detected from filename), n_harmonics=10, threshold_percentile=95, chunk_sec=2.0 s STFT window.
Stage C: Complex Spectral Hampel Interpolation
FFT-domain rolling-median outlier detection: computes magnitude spectrum, applies median filter (window=2.0 Hz), identifies bins where |X[f] - median| > 3 × 1.4826 × MAD.
Preserves complex phase: outlier bins are attenuated to target level (attenuation_db = −60 dB) while maintaining the original phase angle.
Spectrum-Fit Multi-Harmonic variant: STFT gain mask with cosine taper (half_bw=1.0 Hz rolloff) nulls each harmonic band independently. Achieved: 6.84 dB mean harmonic attenuation (awake), 8.86 dB (sleep).
Surgical FFT spectral interpolation: cubic-spline fit through ±10 reference bins replaces artifact zone (±2 bins ≈ 42 mHz at 256 Hz / 60 s) — narrowest possible removal bandwidth.
[ FIGURE: PSD Before vs. After Artifact Removal ]
Power Spectral Density (Welch, Hann window, nperseg=n_fft, noverlap=nperseg//2) Three panels: RAW DBS | After Stage A (SVD) | After Stage C (Hampel) X-axis: 0–45 Hz Y-axis: power (dB re: µV²/Hz) Vertical dashed lines at 7 Hz harmonics; shaded beta band (13–30 Hz) Source file: results/figures/psd_comparison_awake.png
BIOMARKER EXTRACTION
Frequency-Domain Biomarker Isolation
Beta Band Power (13–30 Hz)
Power Spectral Density via Welch's method: Hann window, nperseg=n_fft, 50% overlap (noverlap=nperseg//2).
Band power = Simpson's rule integration of PSD over [13, 30] Hz per electrode per epoch.
Beta is the primary biomarker of STN motor circuit engagement; pathological beta synchrony (>30 µV²/Hz) correlates with Parkinsonian rigidity.
Benchmark result: Spectrum-Fit method retained only 12.4% of beta-band power (awake) vs. 94.5% for Time-Domain Hampel — critical tradeoff driving the hybrid approach.
Phase-Amplitude Coupling (PAC)
Measures modulation of high-frequency amplitude (beta: 13–30 Hz) by the phase of low-frequency oscillation (theta: 4–8 Hz) using the Modulation Index (MI).
MI = |Σ A(t)·exp(iφ(t))| / N, where A(t) = instantaneous beta envelope (Hilbert), φ(t) = theta instantaneous phase.
Theta–beta PAC reflects cortico-subthalamic communication; elevated coupling distinguishes DBS therapeutic states from untreated Parkinson's baseline.
Topographic PAC maps computed across all 19 electrodes; frontal-central electrodes (Fz, Cz, FCz) show highest coupling magnitude in DBS-on recordings.
Additional Features for ML Feature Vector
Delta (0.5–4 Hz), Theta (4–8 Hz), Alpha (8–13 Hz), Gamma (30–80 Hz) relative band powers per electrode.
19-channel topographic maps (MNE standard_1020 montage) provide spatial distribution features for CNN input.
MACHINE LEARNING IMPLEMENTATION
Feature Engineering & Classification Pipeline
Feature Vector Construction
Per-epoch feature vector (2-second non-overlapping windows, 256 samples):
5 relative band powers × 19 electrodes = 95 spectral features
PAC Modulation Index per electrode = 19 coupling features
Beta asymmetry index (left vs. right hemisphere) = 1 feature
Total: 115-dimensional feature vector per epoch, z-score normalized across training set.
Model 1: Support Vector Machine (SVM)
Kernel: Radial Basis Function (RBF); C=1.0, gamma=scale (Scikit-learn default).
Task: Binary classification — awake vs. sleep state using post-artifact-removal EEG features.
Train/test split: 80/20 stratified; 5-fold cross-validation for hyperparameter selection.
Model 2: Random Forest (RF)
n_estimators=100, max_features=sqrt; provides feature importance ranking for biomarker interpretability.
Feature importance confirms beta power (Cz, FCz) and theta-beta PAC as top discriminative features across states.
Model 3: Convolutional Neural Network (CNN)
EEGNet-inspired architecture: depthwise separable convolutions over (channels × time) input (19 × 256).
Input: cleaned EEG epochs directly (raw time-series) bypassing manual feature extraction.
Architecture: Conv2D(F1=8, kernel=(1,64)) → DepthwiseConv2D(D=2) → SeparableConv2D(F2=16) → FC(2); dropout=0.25.
Trained with Adam optimizer (lr=1e-3), categorical cross-entropy, batch_size=32, 50 epochs.
[ FIGURE: RF Feature Importance — Top 20 Features ]
Horizontal bar chart: features ranked by mean decrease in impurity Top features highlighted: beta_Cz, beta_FCz, pac_Fz, alpha_Pz Color-coded by feature type (band power / PAC / asymmetry) Source: RF model.feature_importances_ on held-out test set
RESULTS
8.86 dB
Mean Harmonic Attenuation (Sleep, Spectrum-Fit)
98.3%
Broadband Preservation (Time-Domain Hampel)
94.5%
Beta-Band Retention (Hampel Time-Domain)
12.4%
Beta Retention (Spectrum-Fit — tradeoff)
Key Findings
Hybrid pipeline achieves best tradeoff: SVD subspace projection removes phase-locked DBS structure; Spectral Hampel attenuates residual harmonics (6.84 dB mean awake); Time-Domain Hampel preserves broadband brain (97.1%).
Zapline+ (spectro-spatial eigendecomposition): near-zero attenuation at fundamental 7 Hz (0.68 dB awake) but best broadband preservation (76.96%) — suitable only as refinement step.
CNN-DAE achieves highest harmonic SNR (−26.2 dB) with 176.6% theta retention but 28.7 s/epoch runtime — prohibitive for real-time closed-loop applications.
Beta-band power (13–30 Hz) is the most discriminative feature for SVM/RF classification of awake vs. sleep state, consistent with established STN biomarker literature.
PAC (theta phase → beta amplitude) shows consistent modulation in DBS-on epochs at frontal-central electrodes, corroborating cortico-subthalamic coupling as a viable biomarker.
[ FIGURE: Per-Harmonic Attenuation Comparison (Bar Chart) ]
Grouped bar chart: attenuation (dB) at 7, 14, 21, 28, 35, 42 Hz Groups: SVD (Sinusoidal Reg), Spectrum-Fit, Freq-Hampel, Zapline Spectrum-Fit: 0.5 / 13.95 / 24.51 / 27.26 dB at 7/14/28/42 Hz Source: results/metrics/harmonic_attenuation_*_awake.csv
CONCLUSION
A hybrid SVD subspace + NLMS adaptive + Spectral Hampel pipeline provides clinically viable DBS artifact removal, balancing attenuation strength and beta-band preservation.
Beta-band power (13–30 Hz) and theta–beta PAC are robust, discriminative biomarkers recoverable from post-DBS EEG using the hybrid pipeline.
SVM and Random Forest classifiers achieve reliable awake/sleep state classification from extracted biomarkers, with RF feature importance confirming fronto-central beta dominance.
Future work: real-time Dagster pipeline orchestration, CNN-EEGNet end-to-end training on larger DBS cohorts, and integration with closed-loop DBS control systems.
References: Allen et al. (2010) Clin. Neurophysiol. | Chen et al. (2022) J. Neural Eng. | MNE-Python 1.10.2 | Scikit-learn 1.x | EEGNet (Lawhern et al. 2018) | Modulation Index (Tort et al. 2010)
wanghleys@gmail.com | github.com/wanghley/ml-driven-eeg-biomarkers | Duke University Spring 2026